## Slide 1
Lower Mississippi
RIVER FORECAST CENTER
LMRFC Reference Slide For Crest Tables
LMRFC Forecasts Issued Morning of March 29, 2021
Talking Points
Over the weekend, five to eight inches of rainfall fell over middle Tennessee and significant rises are occurring on the Cumberland and Tennessee Rivers. Minor to moderate flooding is expected on the lower Ohio River with Cario, IL expected to crest at 47.0ft on April 4th. This crest would be ½ foot higher than the two previous crests that occurred this month.
On the middle Mississippi River above the junction with the Ohio River, minor flooding will continue at Cape Girardeau, MO for several more days before falling below flood stage by this weekend.
On the lower Mississippi River above the junction with the Arkansas River, minor flooding will continue from New Madrid, MO to Osceola, AR and at Mhoon Landing, MS. Rises of 1 to 2 feet will occur over the next 7 to 10 days as routed water from the lower Ohio River continues to work downstream.
On the lower Mississippi River below the junction with the Arkansas River, moderate flooding will continue at Natchez, MS and minor flooding will continue from Arkansas City, AR to Vicksburg, MS and from Red River Landing, LA to Baton Rouge, LA. The peak flows from the Arkansas River are starting to enter the lower Mississippi River. Arkansas City, AR should crest over the next couple of days and the crest should approach New Orleans, LA by the end of the weekend.
Crests on the lower Mississippi River between Arkansas City, AR downstream to New Orleans, LA will crest on flows from the Arkansas River and before the routed water from the lower Ohio River. The routed water from the lower Ohio River will fill in behind the current crests and keep stages elevated through April.
The 16 day future rainfall model shows the same crests as the official forecast on the lower Ohio and Mississippi Rivers.

## Slide 2
Ohio/Mississippi River Crest Watch
Lower Mississippi River Forecast Center weather.gov/lmrfc
NWSLMRFC
@NWSLMRFC
Bonnet Carré Location
Created March 29 2021 @ 12:00 pm CDT
MS River at Caruthersville
Current: 33.3’ MINOR
Forecast:
MS River at Memphis
Current: 30.5’ ACTION
Forecast:
Crest in ACTION at 31.0’ on April 27th
MS River at Natchez
Current: 51.1’ MODERATE
Forecast:
Crest in MODERATE at 52.5’ on April 2nd
5 Days
MS River at Ark City
Current: 37.4’ MINOR
Forecast
Crest in MINOR at 38.0’ on March 31st
MS River at Vicksburg
Current: 43.9’ MINOR
Forecast:
Crest in MINOR at 45.5’ on April 1st
0.5 Day
2 Days
2 Days
1 Day
2 Days
2 Days
2 Days
OH River at Paducah
Current: 35.7’ ACTION
Forecast:
Crest in MINOR at 41.0’
on April 4th
OH River at Cairo
Current: 44.0’ MINOR
Forecast:
Crest in MODERATE at 47.0’ on April 4th
MS River at Greenville
Current: 48.2’ MINOR
Forecast:
MS River at New Orleans
Current: 13.8’
Forecast:
Crest at 15.0’ on
April 4th
MS River at Baton Rouge
Current: 36.0’ MINOR
Forecast:
Crest in MINOR at
37.5’ on April 4th
Morganza Location
Crest in MINOR at 49.0’
on March 31st
Crest in MINOR at 34.5’
for April 6th