## Slide 1
Lower Mississippi
RIVER FORECAST CENTER
LMRFC Reference Slide For Crest Tables
LMRFC Forecasts Issued Morning of March 10, 2023
Talking Points
The USACE determined that the Cairo, IL gage had been reporting incorrect stage levels and they made an adjustment today of approximately 1.5 ft to correct the stages.
The lower Ohio River has crested at all locations and minor flooding at Olmsted Lock & Dam, IL and Cairo, IL should end by the middle of next week.
On the lower Mississippi River, cresting conditions are near Caruthersville, MO and should reach Memphis, TN later this weekend.
Minor flooding is still forecast for Red River Landing, LA and this location is not expected to crest until next weekend.
The 16 day future rainfall guidance shows continued falls on the lower Ohio River through the third week of March and then steady river levels by the end of the month. The model does not show any renew flood crests through the first week of April.

## Slide 2
Ohio/Mississippi River Crest Watch
Lower Mississippi River Forecast Center weather.gov/lmrfc
NWSLMRFC
@NWSLMRFC
Bonnet Carré Location
Created March 10 2023 @ 12:00 pm CDT
MS River at Caruthersville
Current: 32.2’ MINOR
Forecast:
MS River at Memphis
Current: 27.4’
Forecast:
Crest in ACTION at 28.5’ on March 12th
MS River at Natchez
Current: 45.1’ ACTION
Forecast:
Crest in ACTION at
47.5’ on March 18th
5 Days
MS River at Ark City
Current: 32.4’
Forecast
Crest at 34.2’ on
March 15th
MS River at Vicksburg
Current: 38.0’ ACTION
Forecast:
Crest in ACTION near 40.3’ on March 16th
0.5 Day
2 Days
2 Days
1 Day
2 Days
2 Days
2 Days
OH River at Paducah
Current: 37.1’ ACTION
Forecast:
Crested and falling over the next 5 days.
OH River at Cairo
Current: 43.8’ MINOR
Forecast:
Crested and falling below MINOR on March 14th
MS River at Greenville
Current: 42.4’ ACTION
Forecast:
MS River at New Orleans
Current: 11.2’
Forecast:
Crest at 12.2’ on
March 20th
MS River at Baton Rouge
Current: 30.5’ ACTION
Forecast:
Crest in ACTION at
33.0’ on March 20th
Crest Location
Crest in ACTION near 44.2’
on March 15th
Cresting now and falling below MINOR on March 12th